| Security DESIGN CRITERIA | DC 2.10 |
| --- | --- |

2.10.1	Security Gates

2.10.1.1	If security controls are required to prevent access to upper floors in buildings that have open exterior stairs and exterior exit balconies, use security gates at ground floor level.  Gates must be capable of being locked in the open position, and also must be able to open from the interior in an emergency without any special tools or keys to avoid inadvertent entrapment.  Do not use roll-up doors without prior approval by Project Coordinator.

2.10.2	Avoiding Built-in Security Problems

2.10.2.1	Avoid materials and/or configuration of construction that can be used as ladders or aiding a person to climb onto or into buildings.  Some examples of these are:

a.	Opening in block walls or other fenestration extending from ground to roofs.

b.	Downspouts that can be grasped or grabbed.

c.	Foot and hand-holds, such as large fixed vent louvers, in walls of buildings without roof overhangs.

d.	Low roofs, canopies, eyebrows, etc., which are accessible from the ground and in turn provide access to upper building levels.

e.	Open stairs or balconies readily accessible from stairway landings or ground floor railings.