| Soil Treatment for Vegetation Control TECHNICAL GUIDE | TG 02362 |
| --- | --- |

1.	COORDINATION ISSUES: (Not used)

2.	DESIGN ISSUES: (Not used)

3.	DRAWING NOTES: (Not Used)

4.	STANDARD DRAWINGS: (Not Used)

5.	SPECIFICATION NOTES: (Not Used)

6.	GUIDE SPECIFICATION:

6.1	Specification Paragraphs:  As of 03/2003, a complete Guide Specification for Soil Treatment for Vegetation Control is no longer being maintained by DAGS.  The Consultant shall utilize the following specification paragraphs and information as appropriate in the development of the Project Specifications.

6.2	General Requirements (Part 1)

6.2.1	Work included:  spraying weed killer on the prepared roadway subgrade prior to the installation of the base course and where called for on the drawings and also on existing growth prior to application of asphalt in the case of resurfacing jobs.

6.3	Submittals (Part 1)

6.3.1	Submit material product data and Material Safety Data Sheets.

6.4	Materials (Part 2)

6.4.1	Weed Killer:   "Casoron 4G", "Norosac 4G", for under asphalt application on new or rebuilt pavement, and shall be "Hyvar X", "Roundup" for application to existing weeds for resurfacing jobs.

6.5	Application (Part 3)

6.5.1	Mix the under asphalt weed killer and uniformly spread using calibrated application equipment at the maximum rates permitted for under asphalt use. Install base course material as soon as possible after applying the weed killer to preclude loss of germination inhibiting action.

6.5.2	In treatment of existing growth on resurfacing jobs, mix the weed killer and uniformly spray.

6.5.3	Retreat nut grass and weeds two (2) days after initial application and again if growth still exists.

6.5.4	Notify the Contracting Officer 24 hours before application of weed killer.

END OF SECTION 02362