| Custom Cabinets TECHNICAL GUIDE | TG 06410 |
| --- | --- |

1.	COORDINATION ISSUES:

1.1	Refer to TG E 2010.01 FIXED CASEWORK.

1.2	Refer to TG 06070 WOOD TREATMENT.

2.	DESIGN ISSUES:

2.1	Countertop and Shelving Support:  Countertops and shelving shall be properly supported to prevent sagging.

2.2	Countertop depth:  Countertops shall be of sufficient depth (width) to accommodate the equipment that will be used. For example, consider the depth requirement for the computer CPU, monitor and keyboard along with the appurtenant wiring and cables.

2.3	User’s Needs:  Shelving and drawers shall be provided to suit the user's requirements.

3.	DRAWING NOTES:   (Not Used)

4.	STANDARD DRAWINGS:    (Not Used)

5.	SPECIFICATION NOTES:

5.1	General:  Due to recurring maintenance and security problems involving door hardware, address the following items.

5.1.1	Cabinet Hardware:

5.1.1.1	Hinges:  Where concealed “European” type door hinges  (e.g. Grass, Salice, Blum) are specified or intended to be used, the specifications shall clearly indicate that the hinges shall permit the doors to swing open a minimum of 160 degrees (to prevent the pull-out of screw fasteners).  Do not specify pivot-type hinges.

5.1.1.2	Catches:

a.	A storage cabinet double door shall have its inactive leaf secured with slide bolts at the top and bottom of the door.

b.	Wall cabinet shall have its catch located at the bottom of the door. Door catches shall not be located out of reach at the tops of the doors.

5.1.1.3	Keying:  Identify which locks are to be "keyed-alike". (Coordinate requirements with the user through the project coordinator.)

a.	All lockable cabinets within a room shall be keyed-alike.

b.	Where the cabinet lock and the entrance door lock operate on the same key, they shall be keyed-alike.

6.	GUIDE SPECIFICATION: (Not Used)

END OF SECTION 06410