| Operable Partitions TECHNICAL GUIDE | TG 10650 |
| --- | --- |

1.	COORDINATION ISSUES:

1.1	Contract Time:  Consultant shall account for required lead time when establishing the Contract Time in the Proposal, TG 00400.

2.	DESIGN ISSUES:

2.1	Operable vs. Accordion

2.1.1	General:  Operable partitions, either single or folding panels, are often utilized over accordion partitions due to their higher STC ratings and shallow depth when stacked. However, due to their size and weight, these partitions are difficult to operate and maneuver into position by a single person. Additional help from custodial staff or others is often required, taking them away from their work. This has a serious implications especially in classrooms and other spaces where the panels are moved on a daily basis.

2.1.2	Selection:  Therefore, because of their ease of use and operation, accordion partitions shall be used in lieu of single or folding panel partitions where their STC level is sufficient and the room configuration can accommodate its stacked depth.

2.1.3	Other Considerations:  Where the use of either type of partition is contemplated, the designer should also consider the following:

2.1.3.1	Minimum STC rating required between classrooms = 43.

2.1.3.2	The impact of the partition on cross ventilation (where the room is naturally ventilated).

2.1.3.3	The design of the structural support to accommodate the weight of the partition within deflection limitations to prevent sagging and binding.

3.	DRAWING NOTES:

3.1	Configuration:  Indicate on drawings.

3.2	Structural Supports: Detail on drawings.

4.	STANDARD DRAWINGS: (Not Used)

5.	SPECIFICATION NOTES:

5.1	Specification Paragraphs:  As of 03/2003, a complete Guide Specification for Movable Partitions is no longer being maintained by DAGS.  The Consultant shall utilize the following specification paragraphs and information as appropriate in the development of the Project Specifications.

6	GUIDE SPECIFICATION:

6.1	Submittals (Part 1):

6.1.1	Submit 8 sets of shop drawings, samples and manufacturer's literature for review.  Allow adequate time to order materials promptly, as this is a long lead item.

6.1.2	The contract drawing details are intended only as a guide to the installation and operation of the partition.  If modifications are necessary for the partition being proposed, the Contractor is responsible to insure that these modifications are planned for and made at no additional cost to the State.

6.2	Acceptable Products (Part 2):

6.2.1	Modernfold - "Acousti-Seal" Model 931 and 932.

6.2.2	Hough Manufacturing Corp.  - "Hufcor" Series 5530R or 5630R with lateral support at the floor for each panel.

6.2.3	Advanced Equipment Corp.  - Type 2MS with lateral support at the floor for each panel.

6.2.4	Approved substitution.

6.3	Materials: (Part 2)

6.3.1	Configuration:

6.3.1.1	Single movable panels or hinged in pairs.

6.3.1.2	Single parting or bi-parting as shown on the drawings.

6.3.1.3	End stacked, side or center as shown on the drawings.

6.3.2	Partition STC rating:  not less than 43 when tested in accordance with ASTM E90; or an NSSEA acoustical rating of Class F.

6.3.3	Provide positive lateral stability for panels when positioned for use, both individually and severally, by floor guides, telescoping seals, or other such system.

6.3.4	Panel facing: 22 gauge minimum steel.

6.3.5	Finish: baked enamel or, at the option of the manufacturer, faced with vinyl fabric weighing not less than 29 oz. per 54" wide lineal yard.

6.3.6	Include all hardware, hangers, floor tracks where standard with the manufacturer, jambs, anchors and guides; and include provision for adjustments necessary for a satisfactory installation.

6.3.7	Markerboard and tackboard: include as indicated on the elevations and as standard with the door manufacturer. Include all necessary trim to make fixed installation. Mounting shall be as recommended by the manufacturer.

END OF SECTION 10650