| Asbestos Containing Building Materials (ACBM) TECHNICAL GUIDE | TG 13281 |
| --- | --- |

1.	COORDINATION ISSUES:

1.1	Renovation work requires more asbestos survey information and design requirements than what was previously considered adequate. Where painting, electrical rewiring, wall modifications, etc. are specified for a project, testing in addition to the normal asbestos surveys must be done prior to the design.

1.1.1	If the project is going to disturb joint compounds, supplemental survey information must specifically address asbestos levels in the joint compounds only, not just as a composite with the wallboard. (This is a new procedure that asbestos inspection consultant have not been doing!).

1.1.2	If the joint compound contains any detectable (even if it is below the EPA's 1% threshold) asbestos you must use Section 01100 Summary to inform the contractor where the asbestos containing joint compounds were located. (This is the same procedure used for other asbestos building materials.)

1.1.3	Asbestos type engineering controls (i.e. keeping debris wet, etc.) must be specified to try to keep the exposure below the Hawaii permissible exposure limit. (Use a certified asbestos designer.)

1.2	Reason for this Technical Guide

1.2.1	Current asbestos surveys are based on the testing procedures of the Asbestos Hazard Emergency Response Act (AHERA). The rules enforced by this act are targeted at protecting the environment. However, from an occupational exposure and enforcement point of view the Hawaii Occupational Safety and Health (HIOSH) can extend similar rules to construction locations that may not be covered under the EPA rules. A significant number of our building renovation sites may be regulated by HIOSH even when they are not regulated by the EPA.

1.2.2	It is important to realize that the trigger point for HIOSH is fundamentally different than that used by the Environmental Protection Agency (EPA). AHERA requires samples of building materials to define an amount of asbestos in the material which may be a composite such as wallboard system. On the other hand, HIOSH samples the environmental air quality breathed by the employees during the work process.

1.2.3	Asbestos containing joint compounds not normally identified by the AHERA sampling procedures have been found to cause HIOSH defined occupational exposures when sanded, drilled, or sawed. When this happens most of the AHERA mandated containment (e.g. negative air, etc.) and work practice (e.g. disposal, cleanup, etc.) procedures are required of the contractor by HIOSH Rules under Hawaii Statutes.

2.	DESIGN ISSUES: (Not Used)

3.	DRAWING NOTES: (Not Used)

4.	STANDARD DRAWINGS: (Not Used)

5.	SPECIFICATION NOTES: (Not Used)

6.	GUIDE SPECIFICATION: (Not Used)

END OF SECTION 13281