| Lead-Based Paint Control Measures TECHNICAL GUIDE | TG 13282 |
| --- | --- |

1.	COORDINATION ISSUES:

1.1	For all projects where existing paint will be disturbed in buildings constructed prior to 1978, a consultant certified by the EPA as a Lead Project Designer or Lead Supervisor shall be employed.  Consultant shall be certified in accordance with 40 CFR 745 Subpart L.

1.2 	Consultant shall determine whether testing for lead-based paint will be done.

1.3 	If it is determined or assumed that lead-based paint will be disturbed, a specification section “13282 - Lead-Based Paint Control Measures” shall be developed to deal with the lead-based paint hazards.  Throughout this Technical Guide, lead-based paint is defined as paint containing lead in any amount.

1.4 	The classification of the lead-based paint as hazardous waste must be performed in accordance with 40 CFR 261, and in the design phase of the project.  This classification is prerequisite to the requirement of special handling, storage, and disposal according to Federal and local hazardous waste management regulations.

1.5 	A site visit shall be required so that appropriate provisions can be included in the design.

1.6 	Evaluated whether building occupants need to be relocated during lead paint disturbance.

2.	DESIGN ISSUES:

2.1	Project shall conform to all federal, state, and local regulations.

2.2	All the requirements for 40 CFR 745 Subpart L shall apply even though the building does not meet the regulation’s definition of “Target Housing” or “Child-occupied Facility.”  In other words, all facilities shall be considered to be covered by the regulations in 40 CFR 745 Subpart L.  Therefore, all projects should have wipe sampling and all workers need to be certified.

3.	DRAWING NOTES:

3.1	Drawings should indicate the location, extent, and condition of lead-based paint to be removed or disturbed.  Clearly indicate if lead-based paint is to be removed to the substrate.

4.	STANDARD DRAWINGS: (Not Used)

5.	SPECIFICATION NOTES:

5.1	Lead Supervisor.  The Contractor shall employ a person certified as a Lead Supervisor in accordance with 40 CFR 765 Subpart L.  The Lead Supervisor shall perform the following:

5.1.1	Certify training as meeting all federal, state, and local requirements.

5.1.2	Review and approve lead-based paint disturbance/removal plan for conformance with applicable standards.

5.1.3	Provide the proper notifications to the Contracting Officer, State Department of Health, and the EPA prior to starting work.

5.1.4	Continuously inspect lead-based paint removal work for conformance with the approved plan and specifications.  Prepare a daily log of all lead disturbance work done.

5.1.5	Perform air and wipe sampling.

5.1.6	Control work to prevent hazardous exposure to human beings and to the environment at all times.

5.1.7	Collect required submittals.

5.1.8	Compile the Abatement Report.

5.2	Specify the location (doors, windows, walls, ceilings, floors, piping or building materials), extent (specific surfaces or components) and condition (intact, flaking, chalking, alligatored, chipped, peeling) of lead-based paint to be removed or disturbed.

5.3	Submittals

5.3.1	Testing Laboratory Qualifications.  Name, address, and telephone number of testing laboratory selected to perform the air, wipe, and soil sampling, testing, and reporting of airborne concentrations of lead.  Use a laboratory accredited under the EPA National Lead Laboratory Accreditation Program (NLLAP) by either the American Association for Laboratory Accreditation (A2LA) or the American Industrial Hygiene Association (AIHA) and that is successfully participating in the Environmental Lead Proficiency Analytical Testing (ELPAT) program to perform sample analysis.

5.3.2	Lead Supervisor documentation.  Submit documentation that Lead Supervisor is certified in accordance with 40 CFR 765 Subpart L.

5.3.3	Training certification.  Submit documentation for each employee that they are certified in accordance with 40 CFR 765 Subpart L.

5.3.4	Lead-based paint disturbance/removal plan.  Include “Written Compliance Program” required by 29 CFR 1926.62 (e) (2) and “Occupant Protection Plan” required by 40 CFR 765 Subpart L as part of this plan.

5.3.5	Environmental Sampling Results.  Submit sampling results to the Contracting Officer within 3 working days of collection, signed by the testing laboratory responsible official, the employee that performed the sampling, and the Lead Supervisor.

5.3.6	Product data and Manufacturers Instructions for all equipment and materials used.

5.3.7	Rental equipment notification.  If rental equipment is to be used during lead-based paint handling, notify the rental agency in writing concerning the intended use of the equipment.  Furnish a copy to the Contracting Officer.

5.3.8	Submit applicable Material Safety Data Sheets for all chemicals used in paint removal work.  Use the least toxic product approved by the Contracting Officer.

5.3.9	Daily log of all lead disturbance work done.

5.3.10	Hazardous Waste Management Plan (if hazardous waste is generated)

5.3.10.1	Identification and classification of hazardous wastes associated with the work.

5.3.10.2	EPA Generator Identification Number for the site.

5.3.10.3	Estimated quantities of wastes to be generated and disposed of.

5.3.10.4	EPA Transporter Identification Numbers, names, and qualifications of each contractor that will be transporting, storing, treating, and disposing of the wastes.

5.3.10.5	Names and qualifications (experience and training) of personnel who will be working on-site with hazardous wastes.

5.3.10.6	List of waste handling equipment to be used in performing the work, to include cleaning, volume reduction, and transport equipment.

5.3.10.7	Spill prevention, containment, and cleanup contingency measures including a health and safety plan.

5.3.10.8	Work plan and schedule for waste containment, removal, and disposal.  Wastes shall be cleaned up and containerized daily.

5.3.10.9	Unit cost for hazardous waste disposal according to this plan.

5.3.11	Hazardous Waste Disposal Documentation.  If hazardous waste is being disposed of, submit written evidence that the hazardous waste treatment, storage, or disposal facility is approved for lead disposal by the EPA and State or local regulatory agencies.  Submit one copy of the completed manifest, signed and dated by the initial transporter in accordance with 40 CFR 262.

5.3.12	Dump receipts from landfill operator.

5.3.13	The Contractor shall complete the Hazardous Waste Disposal Log and the Project Hazardous Waste Log for each site.  See Appendix A and Appendix B of this Section for the format of these logs.

5.3.14	Provide copy of the contract plans and specs to the User Agency for record keeping purposes.

5.4 	Lead Control Area Requirements:

5.4.1.	If lead-based paint will be removed by means which will not likely create airborne, lead-containing dust (such as careful wet scraping or chemical stripping), establish a lead control area by situating critical barriers and physical boundaries around the area or structure where lead-based paint removal operations will be performed.

5.4.2.	If the removal practice will create airborne dust, create a full containment with critical barriers, HEPA filtered exhaust, negative pressure enclosure, and decontamination facilities.

5.4.3.	Vent local exhaust outside the building only and away from building ventilation intakes.

5.4.4.	Lead control area should ensure airborne lead levels are below action level outside the area.

5.5	Heating, Ventilating, and Air conditioning Systems that supply, exhaust, or pass through the lead control area should be shut down, locked out, and isolated.

5.6	Surfaces and equipment that won’t be painted shall be covered with poly during lead paint disturbance.  After work is completed, repair all damage from fastening and sealing and remove all residual adhesive from surfaces.

5.7	Environmental Sampling During paint removal work.  Lead Supervisor shall conduct area air sampling daily, on each shift in which lead-based paint removal operations are performed, in areas immediately adjacent to the lead control area.  Sufficient area monitoring shall be conducted to ensure unprotected personnel are not exposed at or above the action level.  If action level is reached, stop work and correct conditions causing the high levels.  Resume only after approval of the Lead Supervisor and the Contracting Officer.  Cost of retesting shall be borne by the contractor.  For outdoor operations, at least on sample on each shift shall be taken on the downwind side of the lead control area.  The consultant shall determine the location and number of samples taken.

5.8	Hazardous and non-hazardous waste shall be segregated as much as feasible.  The Contractor shall be responsible for all waste disposal including hazardous waste.  No additional compensation will be made for waste disposal.

5.9	Wastewater shall be sampled to determine whether the wastewater can be disposed of in County sewer system.  Wastewater shall not be disposed of in storm drain or dumped on ground regardless of test results.

5.10	Payment for disposal of hazardous waste will not be made until a signed copy of the manifest from the treatment or disposal facility certifying the amount of lead-containing materials delivered is returned and a copy is furnished to the Contracting Officer.

5.11	Clearance Wipe Sampling.  Shall be performed as described in 40 CFR 745 Subpart L by the Lead Supervisor.  All retesting resulting from elevated lead results shall be done at no additional cost to the State.

5.12	Abatement Report.  An abatement report shall be submitted as required by 40 CFR 745 Subpart L.  In addition to the requirements in 40 CFR 745 Subpart L, the Abatement Report shall include all items listed under Submittals (Item 5.3).  3 copies shall be submitted (1 each for user agency, project file, Quality Control Branch).  Final payment shall not be made until this document is furnished.

6.	GUIDE SPECIFICATION:  (Not Used)

TG 13282 APPENDIX A

HAZARDOUS WASTE DISPOSAL LOG

Name of Facility

Street Address

City, State, Zip

| MONTH/YEAR | DESCRIPTION OF HAZARDOUS WASTE | APPROXIMATE WEIGHT IN POUNDS | SPECIAL HANDLING |
| --- | --- | --- | --- |

TG 13282 APPENDIX B

PROJECT HAZARDOUS WASTE LOG

(Contractor to complete one per site)

PROJECT:		____________________________________________________________________

____________________________________________________________________

D.A.G.S. JOB NO.:____________________________________________________________________

START DATE:	_____________________	COMPLETION DATE:	_____________________

GENERAL CONTRACTOR:	_________________________________________________________

ADDRESS:	____________________________________________________________________

____________________________________________________________________

TELEPHONE:	___________________	FAX NUMBER:	_____________________

NAME OF SUPERINTENDENT FOR THIS PROJECT:	____________________________

NAME OF GENERATOR (FACILITY):	______________________________________________

ADDRESS:	____________________________________________________________________

____________________________________________________________________

TELEPHONE:	___________________	FAX NUMBER:	_____________________

DESCRIPTION OF HAZARDOUS WASTE:		_______________________________________

______________________________________________________________________________________

APPROXIMATE WEIGHT (IN POUNDS):	_____________________

MONTHLY DISPOSAL LOG:

MONTH:	___________________	WEIGHT IN POUNDS:	_______

MONTH:	___________________	WEIGHT IN POUNDS:	_______

MONTH:	___________________	WEIGHT IN POUNDS:	_______

DISPOSAL SITE:		________________________________________________________________

CONTRACTOR DISPOSING OF HAZARDOUS WASTE:	____________________________

ADDRESS:	____________________________________________________________________

____________________________________________________________________

TELEPHONE:	___________________	FAX NUMBER:	_____________________

DISPOSAL CONTRACTOR IS A (CHECK ONE OF THE FOLLOWING):

CONDITIONALLY EXEMPT SMALL QUANTITY GENERATOR 	_______

SMALL GENERATOR											_______

LARGE GENERATOR											_______

…………………………………………………………………………………………………………………

APPROVAL:

STATE DESIGNATED COMPETENT PERSON:	____________________________________

COMPANY:	_________________________________________________________

ADDRESS:	_________________________________________________________

_________________________________________________________

TELEPHONE NUMBER:		___________________________________________

____________________________________________	_____________________

SIGNATURE										DATE