| Civil DESIGN CRITERIA | DC 2.1 |
| --- | --- |

2.1.1	Applicability of General Notes:  All notes (sewer, water, grading and others) required by the County for permits may not be applicable to State projects.  Therefore,

2.1.1.1	Locate the note on a separate drawing sheet where practical or separated from applicable Project Notes.

2.1.1.2	Label all the notes “[Sewer] [Water] [Grading] [____________] Required for County Permit”.

2.1.1.3	Make sure applicable Project Notes are separated and clearly identified.  Do not duplicate information that is covered by the Specifications or General Conditions.

2.1.2	Reference to Soils Report:  Do not reference or incorporate the Soils Report into the Contract Drawings.  List the reference to the Soils Report under Specification Section 00800 SPECIAL CONDITIONS, paragraph titled “Reports, Site and Subsurface Investigation, Boring Logs.”

2.1.2.1	Make sure the Boring Logs only reference Specification Section 00800 SPECIAL CONDITIONS.  “Boring Logs reproduced from the Geotechnical Investigation Report referenced in Section 008800 SPECIAL CONDITIONS.”

    - Accessibility

      - Refer to DC 2.15 Accessibility for general design requirements.

      - Calculate spot elevations for all exterior accessible routes on vehicular pavement and pedestrian walkways to assure compliance with ADAAG or ANSI as appropriate, and to assure adequate surface drainage.  Indicate the spot elevations on a plan of sufficient scale to clearly define the design intent.

      - Where slopes or cross-slopes of a maximum 2% are allowed by ADAAG or ANSI, the design slopes should be not less than 1.5% to help prevent ponding water.

      - Include the following note on the Civil Drawings:

“Establish finish elevations for all utility structures, frames and covers within accessible routes such that they will be flush with the surface of the adjacent accessible route when work is completed.  The final finish elevation of any such item shall not exceed ¼” above or below the adjacent finish elevation of the accessible route at any point.  Variations in excess of this amount will be considered defective work, and shall be corrected.”