| Drainage and Containment TECHNICAL GUIDE | TG 02600 |
| --- | --- |

1.	COORDINATION ISSUES:  (Not Used)

2.	DESIGN ISSUES:  (Not Used)

3.	DRAWING NOTES:

3.1	Coordination with Existing Utilities: Utilize the following drawing notes and information as appropriate in the development of the Project Construction Drawings.

3.1.1	Prior to the actual work of constructing the drain system, excavate and expose all utility facilities which will be crossed by the new drain lines and verify their elevations with respect to the new drain grades.  Verify elevations of inverts of new drain lines to be connected to the existing drain lines at their points of connections under this requirement.

3.1.2	Should the actual elevation of any existing utility show a possible discrepancy which may affect the alignment and grade of the new drain lines, immediately notify the Contracting Officer and do not proceed with the drain construction until authorized by the Contracting Officer.

4.	STANDARD DRAWINGS:

4.1	Standard Details:  If any details from the STANDARD DETAILS FOR PUBLIC WORKS CONSTRUCTION, dated September, 1984, are to be followed, note the exact detail on plans.

5.	SPECIFICATION NOTES:

5.1	Specification Paragraphs:  As of 03/2003, a complete Guide Specification for Drainage is no longer being maintained by DAGS.  The Consultant shall utilize the following specification paragraphs and information as appropriate in the development of the Project Specifications.

5.2	 Materials, Installation, Trenching and Backfill:   Specify in accordance with the Counties' STANDARD SPECIFICATIONS FOR PUBLIC WORKS CONSTRUCTION dated September 1986,  and STANDARD DETAILS FOR PUBLIC WORKS CONSTRUCTION dated September 1984, except to exclude paragraphs concerning Measurements and Payments as not applicable to this project.

6.	GUIDE SPECIFICATION:

6.1	Final Inspection (Part 3)

6.1.1	Before Final Inspection, ensure storm drain lines and manholes are free from sand, silt or other obstructions.

END OF SECTION 02600