| Exterior Plants TECHNICAL GUIDE | TG 02930 |
| --- | --- |

1.	COORDINATION ISSUES: (Not Used)

2.	DESIGN ISSUES: Provide root barriers for all trees/plants adjacent to buildings, curbs, walkways, traffic islands or other areas where planting may uproot adjacent structures.

3.	DRAWING NOTES: (Not Used)

4.	STANDARD DRAWINGS:

4.1	Tree Guying Alternate. See attached detail, A/TG 02930

4.2	Tree Staking Alternate. See attached detail, B/TG 02930.

4.3	Shrub Planting. See attached detail, C/TG 02930.

5.	SPECIFICATION NOTES:

5.1	Approved backfill mix for trees and shrubs shall consist of one part burned bagasse, 4 parts topsoil, 3 ounces sulphur coated (20-6-12+iron) control release pelleted fertilizer, 6 ounces well rotted cattle manure and 3 ounces (12-23-12) homogenous pelleted fertilizer. Mix thoroughly before backfilling into tree.

6.	GUIDE SPECIFICATION:  (Not Used)

END OF SECTION 02930