| Rough Carpentry TECHNICAL GUIDE | TG 06100 |
| --- | --- |

1.	COORDINATION ISSUES:

1.1	Coordination with TG 06070 Wood Treatment: All Rough Carpentry shall be treated in accordance with TG 06070.

2.	DESIGN ISSUES:  (Not Used)

3.	DRAWING NOTES: (Not Used)

4.	STANDARD DRAWINGS:  (Not Used)

5.	SPECIFICATION NOTES:

5.1	Power Driven Fasteners:

5.1.1	General: Pneumatic, gas and electric powered drivers (nail and staple guns) has become an industry  standard tool and therefore, concerns have been raised regarding their use and the acceptability of the corrosion resistant finishes of the fasteners must be addressed.

5.1.2	Requirements:  With regard to their use, these devices can drive a variety of fasteners including hot-dipped galvanized nails. The following requirements shall be incorporated into the project specifications to address the use of these devices:

5.1.2.1	Fasteners having chipped coatings shall not be used.

5.1.2.2	Lumber shall be flush and tight against each other during fastening operations.

5.1.2.3	Fasteners securing siding, floor and roof sheathing shall be driven flush with the face of the material. Overdriving of the fastener shall be avoided.

5.1.2.4	Where more than 20% of the fasteners are found to be overdriven up to 1/8" deep, or if any fastener is overdriven more than 1/8" deep, additional fasteners shall be driven at a rate of 1 additional fastener for every 2 overdriven fasteners.

5.1.2.5	Where the corrosion resistant coating on the head of the fastener has been chipped by the device in excess of 25%, the fastener shall be removed and replaced. The device shall not be used until its driver has been repaired.

5.1.2.6	Nails shall be of the proper length to suit their particular application (the point of the nail shall not be exposed after being driven).

5.1.3	Power Driven Fastener Finish:  With regard to the acceptability of the fastener's corrosion resistant finish, in accordance with the Uniform Building Code (19917 Edition), Section 2304.3 - Timber Connectors and Fasteners, fasteners for pressure-preservative-treated and fire-retardant-treated wood shall be of hot-dipped zinc-coated galvanized, stainless steel, silicon bronze or copper.  Since all wood, with the exception of all-heart redwood, must be treated to comply with the Section 06070 - Wood Treatment, all nails must meet these requirements.

5.1.3.1	At this time, there are no power driven nails made of silicon bronze or copper.

5.1.3.2	Although there are mechanically galvanized and electrogalvanized nails having additional coatings of passivating chromate and thermoplastic polymer, these fasteners shall not be used as they have not been approved by the City and County of Honolulu Building Department for use in connection with preservative treated lumber.

5.1.3.3	In addition, due to problems with nail pull-out, smooth stainless steel nails shall not be used. "Ring-shank" type stainless steel nails are acceptable.

5.1.3.4	Hot-dipped zinc-coated galvanized fasteners shall conform to ASTM A641, Class 1. Where the hot-dipped zinc-coated fastener is to be used in conjunction with treated wood foundations, its coating weight shall be at least 2.00 oz/sf for the average of specimens tested and 1.70 oz/sf for any individual specimens.

5.1.3.5	When reviewing the product data for proposed fasteners, be advised some manufacturers reference conformance of their product to ASTM A153, Class "D" fasteners (less than 3/8" [0.375"] diameter). Conformance to this standard exceeds the requirements of ASTM A641. The minimum zinc coating weight of the average of specimens tested shall be 1.00 oz./sf and any individual specimen shall be a minimum of 0.85 oz./sf.

6.	GUIDE SPECIFICATION: (Not Used

END OF SECTION 06100