| Hazardous Material Remediation (Attachment C) TECHICAL GUIDE | TG 13280 |
| --- | --- |

REQUIREMENTS FOR ROOF REMOVAL WORK CONTAINED IN THE OSHA STANDARD FOR ASBESTOS CONSTRUCTION (29 CFR 1926)

The following is a summary of new requirements, with paragraph and page numbers as used in the OSHA Standard, of the parts of the Standard concerning roofing work.

Para. No.															Page

1926.1101 Asbestos

(b)	Definitions													41132

Class II asbestos work means activity involving the removal of ACM, which includes roofing and construction mastics.

(c)	Permissible exposure limits (PELs)							41133

(1)	8 hour time weighted average (TWA), .1 f/cc			41133

(2)	Excursion Limit, 30 min., 1.0 f/cc						41133

(Note: Action level, which was .1 f/cc, has been deleted. A discussion on the reasons for this deletion is on page 40974, paragraph (2)).

(e)	Regulated areas												41133

All Class II work must be conducted within a regulated area, demarcated in any manner which limits the number of persons within the area and protects persons outside the area.

(f)	Exposure assessment and monitoring						41133

(2)	Initial Exposure Assessment								41134

Required to be performed by a "competent person" prior to start of work, unless a "negative exposure assessment" has been performed, to ascertain expected exposure during the work.

(iii)	Negative Exposure Assessment							41134

The employer may demonstrate using objective data that the work cannot release airborne fibers in concentrations exceeding the PELs.

(3)	Periodic Monitoring										41134

For Class II work, daily monitoring must be performed within the regulated area unless a "negative exposure assessment" has been made. Exception: If employees are equipped with supplied-air respirators, daily monitoring may be deleted.

(g)	Methods of compliance										41134

(3)	Prohibitions. The following work practices shall not be used.

(i)	High-speed abrasive disc saws that are not equipped with point of cut ventilator or enclosures with HEPA filtered exhaust air.

(ii)	Compressed air used to remove ACM unless used in conjunction with a enclosed ventilation system designed to capture the dust cloud created by the compressed air.

(iii)	Dry sweeping, shoveling or other dry clean up of dust and debris containing asbestos.

(iv)	Employee rotation as a means of reducing employee exposure to asbestos.

(7)	Work practices and engineering controls for Class II work.	41136

(i)	All Class II work must be supervised by a "competent person" (See p. 3 4., this attachment, for definition).								41137

(8)	Additional controls for Class II work					41137

(ii)	For removing roofing material which contain ACM, following work practices apply.

(A)	Intact removal. Remove roofing material in an intact state to the extent

feasible.												41137

(B)	Wet Methods must be used where feasible.			41137

(C)	Cutting Machines shall be continuously misted unless a Competent Person determines that misting substantially decreases worker safety.	41137

(D)	Vacuuming. All loose dust left by a sawing operation must be HEPA vacuumed immediately.								41137

(E)	Handling. Unwrapped or unbagged roofing material must be immediately lowered to the ground.								41137

(F)	Receptacle. Upon being lowered, unwrapped material must be transferred to a closed receptacle in a manner so as to preclude the dispersion of

dust.													41137

(G)	Isolate Air Intakes. Roof level air intakes must be isolated or shut down.

41137

(iii)	Asbestos-Cement Shingles.								41137

(A)	Cutting, abrading or breaking shingles is prohibited unless the employer can demonstrate that methods less likely to result in asbestos fiber release cannot be used.										41137

(B)	Wetting. Spray each panel with amended water (water with surfactant added) prior to removal.								41137

(C)	Handling. Unbagged shingles shall be immediately lowered to the ground via dust tight chutes, crane or hoist. Or bag and lower to ground no later than end of work shift.								41137

(D)	Nails shall be cut with flat, sharp instruments.		41137

(h)	Respiratory protection										41138

Required in the following circumstances:

(ii)		ACM is not removed in an intact state.

(iii)		Removal is not done using wet methods.

(iv)		Employer does not produce a "negative exposure assessment".

(vii)	Employees are exposed above the PELs.

(viii)	In emergencies.

(i)	Protective clothing											41139

Required for any employee exposed to airborne concentrations which exceed the PELs or in cases where a "negative exposure assessment" has not been produced. The transport and cleaning of contaminated clothing is also regulated.

(j)	Hygiene facilitIes												41139

An equipment room adjacent to the regulated area is required for the decontamination of employees and their equipment if a PEL is exceeded or there is no "negative exposure assessment".

(k)	Communication of Hazards									41140

(6)	Signs														41141

Warning signs that demarcate the regulated area shall be provided.

(7)	Labels														41141

All waste containers containing asbestos must be labeled.

(8)	Employee information and training						41141

All employees to handle ACM shall be trained in a course of at least 8 hours.

(l)	Housekeeping													41142

Where vacuum methods are used, HEPA filtered vacuuming equipment must be used.

(m)	Medical surveillance											41142

Required for all persons who are engaged in Class II work for a total of 30 or more days per year, or exposed above the PELs, or required to wear negative pressure respirators.

(n)	Record keeping												41143

Required for objective data relied on for exposure assessments and monitoring, exposure measurements, medical surveillance, training records, and required notifications.

(o)	Competent person											41143

A person designated by the employer as a competent person who has the qualifications and authorities for ensuring worker safety and health. Training of this person shall include all aspects of asbestos removal and handling; such training shall be obtained in a comprehensive course for supervisors.

(q)	Dates															41144

(1)	The standard became effective on October 11, 1994.

(2)	29 CFR 1926.58 remains in effect until the start-up dates of the equivalent provisions of this standard.

(3)	Start up dates. All obligations of this standard commences on the effective date except the following which becomes effective as soon as possible but no later than the following dates:

(i)	Methods of compliance - April 10, 1994.

(ii)	Respiratory protection - February 8, 1995.

(iii)	Hygiene facilities - February 8, 1995.

(iv)	Communication of Hazard - April 10, 1995.

(v)	Housekeeping - January 9, 1995.

(vi)	Medical surveillance - January 9, 1995.

(vii)	Designation and training of a Competent Person - April 10, 1995.

END OF SECTION 13280 - ATTACHMENT C