| Electrical Work TECHNICAL GUIDE | TG 16100 |
| --- | --- |

1.	COORDINATION ISSUES: (Not Used)

2.	DESIGN ISSUES:

2.1	Receptacles:

2.1.1	Specify the types of duplex receptacles in accordance with the following table.  Receptacles shall be of a grade appropriate to the type of facility (i.e. spec/ commercial grade, hospital grade, etc.) and of the proper amperage to service the equipment.

|  | FACILITY / USER | TYPE RECEPTACLE |
| --- | --- | --- |
| A. | Elementary Schools Hospital Wards Mental Institutional Facilities Special Schools (MR) | Grounded Safety Receptacles |
| B. | Secondary Schools University of Hawaii All other public facilities not listed in A. | Grounded Receptacles |
| C. | Restrooms, within 3 feet of sinks and plumbing fixtures, and in exterior locations. | Ground Fault Circuit Interrupting Receptacles |

2.1.2	Where isolated ground receptacles having internal surge protection are provided for computers, if the receptacle has an audible alarm, it shall also be equipped with a silence switch.  Verify with the user for location where such receptacles are required.

2.1.3	Receptacles shall be located so that they are easily accessible (e.g. placed above counters and not below in the undercounter knee space).

3.	DRAWING NOTES:  (Not Used)

4.	STANDARD DRAWINGS: (Not Used)

5.	SPECIFICATION NOTES: (Not Used)

6.	GUIDE SPECIFICATION: (Not Used)